## Slide 1: Testing T3100
Useful Tips and Pointers

## Slide 2: Agenda
T3100 Platform Overview
T3100 – Concepts and Commands to keep in mind
Questions

## Slide 3: T3100 Platform Overview – Single Shelf
Shelf Components
  SMM ( Active / Standby)
  CIM (Active / Standby)
  LIM (Active / Standby)
  CSM (Active / Standby)
  ASM (N+1)

## Slide 4: T3100 Component Users
Accessing the Web GUI provided by the CSM
        https://<system-ip-address>
where <system-ip-address> is the IP address of the T3100. Use USERID/PASSW0RD for access
Accessing the bmcli of the active CSM
        $ ssh USERID@<system-ip-address>
        for admin access
        $ ssh bmsupport@<system-ip-address>
        for support access
Log on to the CSM in slot number 6
        $ ssh –p 12022 <user>@<system-ip-address>
Log on to the CSM in slot number 7
        $ ssh –p 13022 <user>@<system-ip-address>

## Slide 5: T3100 Component Users (Contd)
Accessing the T3100 unix command line
        Login to the CLI as a support user and enter Privileged Mode. Enter the shell command and for the password enter SUPP0RT. You will be logged on to the CLI as the bmsupport user
        support@T3100>en
        support@T3100#shell
    WARNING:…..
    Do you want to continue? (yes or no): yes
    Password: ********
    bmsupport@s01b06 ~]$
Accessing the T3100 unix command line as root
        Login and drop down to the shell as a support user as explained above and switch user to root
    [bmsupport@s01b06 ~]$ su
    Enter the Password as rwelc0me
Accessing the ASM’s as root
        Login and drop down to the shell as a support user as explained above and log on to the ASM blades as root
    [bmsupport@s01b06 ~]$ ssh root@s01b03
    Enter the Password as rwelc0me

## Slide 6: T3100 Component Users (Contd)
SMM
  To SSH into the SMM, use the system IP address, and specify port 22222 for the hardware-level CLI.
    $ ssh –p 22222 <user>@<system=ip-address>
  The SMM provides a hardware-level GUI that you can use for diagnostic and troubleshooting purposes.To access the Support GUI,
        http://<system-ip-address>:22280
LIM/CIM/SEM
  Login and drop down to the shell as a support user as explained above
  You can access the LIM, CIM and SEM via SSH. Hostnames for the switches are in the format s<shelf>i<bay>. For example, the notation s01i07 references the LIM in shelf 1, bay 7.
    [bmsupport@s01b06 ~]$ ssh admin@s01i07
    Enter the Password as welc0me

## Slide 7: VLAN Info – Internal VLANs
CIM (control and management plane)
  1, 4080-4095: reserved
  4085: extension shelf hardware management
  4088: native/untagged for internal management, DHCP/PXE between the ASM and CSM (PVID of all internal ports)
  4089: internal services between the ASM and CSM
  4094: Chassis Internal Network
  4095: reserved for shelf management by the SMM
bmsupport1@OPM-Techn-T3100# show vlan info 1/cim-1/*
Vlan Id State Name Member-Trunks Member-Ports
--------------------------------------------------------------------------
1/cim-1/1 Enabled Default VLAN …
1/cim-1/110 Enabled Interco_Optim_Service_CMI …
1/cim-1/4085 Enabled Extension Shelf Mgmt …
1/cim-1/4088 Enabled Blade Mgmt …
1/cim-1/4089 Enabled Int. Services …
1/cim-1/4094 Enabled CIN …
1/cim-1/4095 Enabled Mgmt VLAN …

## Slide 8: VLAN Info – Internal VLANs
LIM (data plane)
  1, 4080-4095 – reserved
  4081: T2100 access VLAN from ASM and CSM
  4086: internal VRRP
  4087: native/untagged for health-check between the LIM and the ASM (PVID of all internal ports)
  4090: high-speed internal services between the ASM and CSM
  4095: reserved for shelf management by the SMM
bmsupport1@OPM-Techn-T3100# show vlan info 1/lim-7/*
Vlan Id State Name Member-Trunks Member-Ports
--------------------------------------------------------------------------
1/lim-7/1 Enabled Default VLAN …
1/lim-7/4081 Enabled External Caching …
1/lim-7/4086 Enabled VRRP …
1/lim-7/4087 Enabled Health Check …
1/lim-7/4090 Enabled Int. Services …
1/lim-7/4095 Enabled Mgmt VLAN …
1/lim-7/711 Enabled Interco_Optim_Out_Internet …
1/lim-7/712 Enabled Interco_Optim_In_mmsbouygtel …
1/lim-7/713 Enabled Interco_Optim_In_ebouygtel …
1/lim-7/714 Enabled Interco_Optim_In_Exo …

## Slide 9: Interface Bonding
Interface naming scheme: bond[01].<vlan-id>
CSM
  bond0 - Management and control plane
  bond1 - Data plane for connecting to the T2100
ASM
  bond0 - Management and control plane
  bond1 - Data plane

## Slide 10: Checking the ingress / egress Traffic on ASM
Find the ASM handling the traffic using the command
    bmsupport1@OPM-Techn-T3100(diag)# show subscriber blade <subscriber Source-IP>
    <subscriber Source-IP> is mapped to blade: 1/blm-8
    bmsupport1@OPM-Techn-T3100(diag)#
Check the VLAN’s configured in the system for subscriber traffic (data VLAN)
    bmsupport1@OPM-Techn-T3100# show vlan config
    Vlan Id Name Member-Trunks Member-Ports
    ----------------------------------------------------------------------
    primary/cim/110 Interco_Optim_Service_CMI ext1 intx
    primary/lim/711 Interco_Optim_Out_Internet ext3 intx
    primary/lim/712 Interco_Optim_In_mmsbouygtel ext2 intx
    primary/lim/713 Interco_Optim_In_ebouygtel ext2 intx
    primary/lim/714 Interco_Optim_In_Exo ext2 intx
In the example above VLAN 711 is configured as the Internet (egress) and VLAN 712/713/714 are all configured as Subscriber (ingress) depending on the APN used
Use these VLAN information to capture the snoop

## Slide 11: Checking the ingress / egress Traffic on ASM
From the bmcli run the packet-capture command from en->diagnostic
    bmsupport1@OPM-Techn-T3100(diag)# packet-capture blade 1/blm-8/lim/711
    bmsupport1@OPM-Techn-T3100(diag)# packet-capture blade 1/blm-8/lim/713
From the shell run tcpdump to capture the snoop. Use the interface bonding and vlan information to know the exact interface to capture.
  Log on to the T3100 CLI as usual, but as support user
        $ ssh bmsupport@<system-ip-address>
  Drop down to the shell & login to the ASM
    [bmsupport@s01b06 ~]$ ssh root@s01b08
    root@s01b08's password:
    [root@s01b08 ~]# tcpdump -ibond1.711 -s0 -w /var/tmp/egress.pcap &
    [root@s01b08 ~]# tcpdump -ibond1.713 -s0 -w /var/tmp/ingress.pcap &

## Slide 12: Traffic Classification – Bmrule/Bmbypass
Classification rules route data traffic through the T3100
Rules control how incoming packets:
  Get directed to optimization services
  Bypass optimization services
Traffic Classification supports four rule types:
  Bypass
  HTTP
  TCP
  Auto

## Slide 13: Traffic Classification – Bmrule/Bmbypass
Rule order is important. Bypass rules should be listed first
bmsupport1@OPM-Techn-T3100# show traffic-management clsfy-rule
IPv4:
Index Service SrcNetAddr/Mask DstNetAddr/Mask SrcPort DstPort VLAN Enabled
------------------------------------------------------------------------------------
1 http 0.0.0.0/0 0.0.0.0/0 0 80 0 Yes
2 /0 /0 0 0 0 No
3 /0 /0 0 0 0 No
4 /0 /0 0 0 0 No

## Slide 14: Policy Management
T3100 Policy Management provides operators with a rule-based system
The ASMs use Policies to determine how to process subscriber traffic
Every Optimization service on T3100 is dependent on the Policy that is active on the box. Media Optimization, Web Optimization and Media Caching all should be Enable explicitly in the policy. Even if it is configured, if it is not enabled in the policy, it would not be applied. (this is different to that of Unison)

## Slide 15: To run a command on all blades
bmsupport1@OPM-Techn-T3100(diag)# shell
Choice of - */asm-* */blm-* */blm-5 */blm-6 */blm-7 */blm-8 */csm-*
1/asm-* 1/asm-5 1/asm-8 1/blm-* 1/blm-5 1/blm-6 1/blm-7
1/blm-8 1/csm-* 1/csm-6 1/csm-7
bmsupport1@OPM-Techn-T3100(diag)# shell */blm
bmsupport1@OPM-Techn-T3100(diag)# shell */blm-*
bmsupport1@OPM-Techn-T3100(diag)# shell */blm-* "df -h"

## Slide 16: Check Application Processes
bmsupport1@OPM-Techn-T3100# show maintenance process 1/blm-5
Run Level : Running
Process Name PID Restarts Last Start Time
------------------------ ----------- ---------------- ---------------------------
APP-Proxy 19069 1 Wed Jun 12 09:14:16 2013
APP-WebCache 19060 1 Wed Jun 12 09:14:16 2013
CFG-AsmConfig 4770 1 Wed Jun 12 09:14:05 2013
CFG-Blade 4773 1 Wed Jun 12 09:14:05 2013
…
bmsupport1@OPM-Techn-T3100# show maintenance process 1/blm-6
Run Level : Running
Process Name PID Restarts Last Start Time
------------------------ ----------- ---------------- ---------------------------
CFG-ASM 6748 1 Wed Jun 12 13:10:09 2013
CFG-Blade 9845 1 Wed Jun 12 13:10:10 2013
CFG-Csm 6743 1 Wed Jun 12 13:10:09 2013
CFG-CsmData <standby> 3 Mon Jun 24 12:56:21 2013
CFG-DevDb <disabled> 1 Wed Jun 12 13:10:10 2013
…

## Slide 17: Troubleshooting SNMP config
Check that the SNMP Community string is set correctly in the sam.cfg file
    [bmsupport@s01b06 sam]$ pwd
    /opt/bmi/etc/sam
    [bmsupport@s01b06 sam]$ grep "Snmp.TrapCommunity" sam.cfg
    Snmp.TrapCommunity=public
    [bmsupport@s01b06 sam]$
The SNMP Community should be set on all the SMMs, LIMs, CIMs and the Chassis individually. There is no centralized setting for this.

## Slide 18: Centralized repository for Config
The LIM/CIM configs are stored in the centralized repository and are propagated during reboots and restarts.
[bmsupport@s01b06 ~]$ cd /tftpboot/
[bmsupport@s01b06 tftpboot]$ ls -tlr
total 64
dr----x--t 2 root root 4096 Jun 12 13:04 pxelinux.cfg
-rwxr--r-- 1 root root 13148 Jun 12 13:04 pxelinux.0
drwxrwxrwx 3 root root 4096 Jun 12 13:04 1.4.4.3
-rw-r--r-- 1 root root 13705 Jun 24 12:54 c1p3b7-169.254.176.27.cfg
-rw-r--r-- 1 root root 13705 Jun 24 12:54 c1p3b9-169.254.176.29.cfg
-rw-r--r-- 1 root root 3542 Jun 24 12:54 c1p2b1-169.254.176.21.cfg
-rw-r--r-- 1 root root 3542 Jun 24 12:54 c1p2b2-169.254.176.22.cfg
[bmsupport@s01b06 tftpboot]$

## Slide 19: Centralized repository for Firmware Images
The firmware images for the current version are stored in the centralized repository. This should be the firmware version installed on the blades. If not, an issue should be raised.
[bmsupport@s01b06 ~]$ cd /tftpboot/1.4.4.3/images
[bmsupport@s01b06 images]$ ls -tlr ASM200/
total 64912
-rwxrwxrwx 1 root root 2648483 Jun 12 13:04 ibm_fw_uefi_tke124m-1.30_anyos_32-64.uxz
-rwxrwxrwx 1 root root 63818879 Jun 12 13:04 ibm_fw_imm2_1aoo34z-1.85_anyos_noarch.uxz
[bmsupport@s01b06 images]$ ls -tlr LIM/
total 11716
-rwxrwxrwx 1 root root 4308161 Jun 12 13:04 GbESM-24-10G-13.7.10.0_OS.img
-rwxrwxrwx 1 root root 7687332 Jun 12 13:04 GbESM-24-10G-13.7.10.0_Boot.img

## Slide 20: Questions ?